## Slide 1
FEA Lab Project: Static & Transient Analysis
Faizan Munir | ME 1900 | Mechanical Engineering
Instructor: Engr Affan Ahmed Khan

## Slide 2
Introduction & Material Properties
1
Project Overview
This report details Static Structural and Transient Structural analyses on a pentagon-based 3D extruded geometry.
2
Purpose
To observe the structure's response to static and time-dependent varying loads.
3
Material: ME-1900
Young's Modulus: 19000 MPaPoisson's Ratio: 0.28Density: 7850 kg/m³
Material Properties (Static)
Material Properties (Transient)

## Slide 3
Geometry Creation & Meshing
A pentagon shape was sketched on the XY-plane and extruded to a depth of 0.09 m. ANSYS automatically generated a mesh using default controls, including Hex20/Wedge elements.
Sketch (Static)
Extruded Body (Static)
Sketch (Transient)
Extruded Body (Transient)
Mesh Metrics (Static)
Mesh Metrics (Transient)

## Slide 4
Static Structural Analysis
Boundary Conditions
Fixed Support on one face.
Remote Force of 2040 N applied on opposite face (ramped).
Static Results
Equivalent (von-Mises) stress distribution obtained.
Maximum stress visible on the loaded face region.
Convergence not achieved due to large relative change (approx. 19%).
Fixed Support (Static)
Remote Force (Static)
Equivalent Stress (Static)
Convergence Plot (Static)

## Slide 5
Transient Structural Analysis
1
Boundary Conditions
Fixed Support on one face. Five Remote Forces (285 N each) on five different faces.
2
Analysis Settings
Step end time: 1.0 s. Initial time step: 0.2 s. Auto time stepping: ON. Loads follow a triangular ramp-up/ramp-down.
3
Transient Results
Time-based equivalent stress distribution. Max stress: 3.0855e5 Pa at t ≈ 0.21 s, then decreases.
Fixed Support (Transient)
Multiple Remote Forces (Transient)
Analysis Settings + Load Time Graph
Equivalent Stress (Transient)

## Slide 6
Observations & Conclusion
Stress Concentrations
Consistent with applied load faces in both analyses.
Dynamic Response
Transient analysis showed dynamic response to varying loads.
Mesh Quality
Acceptable for student version settings.
Successful Analyses
Both static and transient analyses were successfully performed.
The object behaves predictably under both constant and time-varying loads.